## Slide 1: How to work with this learning material
Power Point
The following power point presents Development trends and innovations in logistics –with a focus on inland navigation . The slides are shortly described in the notes below and you can also find the link to the source if you need further information.
Reader
In addition to the power point presentation, you can also use the reader provided on our platform. It’s more detailed and could be used as a script.
Links
You can also find the sources of our presentation and reader in the links section of the relevant bundled teaching material.
Videos and exercises
There are also videos and exercises, which can be used additionally to this presentation. You can find these videos and exercises separately in the relevant bundled teaching material.
https://www.rewway.at/en/teaching-materials/bundles/ports-and-inland-vessels/

## Slide 2: Learning objectives and target groups
After studying this set of slides, learners will be familiar with the following contents:
The logistics market environment, with the current status quo in logistics and the logistics labour market and the developments in inland navigation
Knowledge of development trends and learn about the 4 drivers for the development of innovations
Knowledge of innovative transport concepts such as synchromodality and physical internet.
Get to know the four areas in which digital business models in logistics are particularly relevant.
target groups:
Secondary school students
University students as an introduction to the topic of developments and innovations in inland navigation

## Slide 3: Development trends and innovations in logistics - focus on inland navigation
Notes: Picture: viadonau in Manual on Danube Navigation p 106, 138.

## Slide 4: Warm-Up-Diskussion Development trends and innovations in logistics – focus on inland navigation
Which current trends are relevant for you in the logistics sector?
Why do you think innovation is of great importance in the inland navigation and logistics sector?
Source: pixabay
What are the drivers for the development of innovative business models?
Notes: The questions mentioned in this slide can serve as a warm-up exercise on the topic of "current development trends and innovations". The answers to these questions can be taken up again and again in the further course of the presentation. Accordingly, they can be taken up and discussed again after the presentation.
Discussion questions (5-10 minutes discussion):
Why do you think innovation is of great importance in inland navigation and logistics?
Which current trends are relevant for you in the logistics sector?
What are the drivers for the development of innovative business models?
Possible support for a discussion:
Fuel
Transport routes
Infrastructure
IT Development
Security
Monitoring
Ships
Green Logistics/PortsTransport concepts
Sustainability
Cooperation
Digitalisation
Picture: www.pixabay.com

## Slide 5: Agenda Development trends and innovation in logistics – focus on inland navigation
Market environment logistics
Development trends at a glance
Innovative transport concepts
Innovative business models
4 Drivers for the development of innovations

## Slide 6: Overview Market environment logistics
For trade and economic development, it is important that goods can be transported:
  secure,
  quickly and
  at low cost
Responsible for the growth of freight transport:
  the rapid increase in global consumption
  boom in online trade several smaller shipments
Source: pixabay
Notes: It is important for national and international trade and economic development that goods are transported safely, quickly and cost-effectively. The rapid growth of freight transport within the EU can be explained by the rapid increase in consumption and a boom in online trade (many smaller consignments).
Source: Der Wirtschaftsingenieur, URL: https://www.der-wirtschaftsingenieur.de/index.php/die-7-dimensionen-der-logistik/ [14.05.2020].
Industriemagazin, URL: https://industriemagazin.at/a/fachkraeftemangel-bei-logistikern-wir-sind-kurz-vor-dem-versorgungskollaps [14.05.2020].
Pciture: www.pixabay.com

## Slide 7: Changes in the transport and logistics industry Market environment logistics
Faster delivery times (same-day-delivery)
Growth in online trade
    digitalisation
    Artificial intelligence and autonomous logistics
    Logistics 4.0
    Supply chain networking
    Multichannel logistics
International cooperation
Notes: The reasons for the changes in the transport and logistics industry are mainly based on the following trends:
Same Day Delivery - delivery on the day of the order. This trend results in poorer utilization of delivery vehicles and increased complexity.
International cooperation and collaboration with the aim of standardizing technical and legal conditions in freight transport
Artificial intelligence & autonomous logistics - this includes, for example, state-of-the-art warehouse robots, self-propelled delivery vehicles or forklifts.
Logistics 4.0.: every item is linked to every other item via the network, resulting in networked department stores, intelligent delivery solutions or even smart refrigerators.
Networking: forwarders become strategic partners and must achieve deeper integration into the customer's supply chain. This can lead to decisive cost advantages for shippers.
Mutichannel logistics: a broader positioning and diversification of distribution logistics channels to make logistics processes more stable and reduce supply risks.
Sources: Industriemagazin, URL: https://industriemagazin.at/a/fachkraeftemangel-bei-logistikern-wir-sind-kurz-vor-dem-versorgungskollaps [14.05.2020].
Transportlogistic, URL: https://www.transportlogistic.de/de/messe/industry-insights/logistikkonzepte-der-zukunft/ [14.05.2020].
T3, URL: https://t3n.de/magazin/innovative-logistik-trends-onlinehandel-zukunftspaket-238987/ [14.05.2020]
WKO, URL: https://www.wko.at/service/aussenwirtschaft/logistik-branche-struktur-zukunft-trends.html [14.05.2020].

## Slide 8: Status Quo in freight transport Market environment logistics
Current situation
  25% of greenhouse gas emissions in Europe come from the transport sector
  77% of freight transport in Europe by road
The European Green Deal
  Reduction of traffic-related emissions by 90% by 2050
  Shifting traffic to environmentally friendly alternatives (inland waterways and rail) will be promoted
  Goal: Climate neutrality
  Automated and connected mobility should help to reduce environmental pollution, especially in urban areas.
Chart: Modal Split in Europe (2020)
| road | rail | inland navigation
Modal Split (EU-27) | 0.75 | 0.18 | 0.07
Notes: The transport sector accounts for 25% of EU greenhouse gas emissions and this figure is rising. Transport emissions must be reduced by 90% by 2050 to achieve climate neutrality. All transport modes will have to contribute to this reduction. Multimodal transport must be promoted to ensure an efficient transport system. To this end, a large proportion of the 77% of internal freight traffic currently carried by road is to be shifted to rail and inland waterways. At present, approximately 17% of all goods are transported by rail and only 6% of all goods are transported by inland waterways. Automated and connected multimodal mobility, together with intelligent traffic management systems made possible by digitisation, should, among other things, help to reduce environmental pollution, especially in urban areas.
Source: Europäische Kommission: Der europäische Grüne Deal, 2019, S. 12f.
Picture: Eurostat, “Freight transport statistics – modal split”, (2020), URL: http://ec.europa.eu/eurostat/statistics-explained/index.php/Freight_transport_statistics_-_modal_split [28.04.2020]

## Slide 9: Labour market Market environment logistics
Significant economic sector and field of activity - high industry growth
Qualified logistics specialists are indispensable
Further development and change of the occupational field through increasing digitalisation
The attractiveness of the occupational field as well as the demand for highly qualified specialists is constantly increasing.
Enormous shortage of skilled workers, especially among mobile staff
Career in logistics - possible through training (apprenticeship) or studies
About 1/6 of the employees in logistics in Germany are academics
Notes: Logistics is important worldwide, both as an economic sector and as a field of activity within companies. It enables the division of labour at home and abroad and thus represents a cornerstone of globalisation. Accordingly, logistics is playing an increasingly important role, making a decisive contribution to the economic success and the success of individual companies. Qualified logistics specialists are therefore indispensable. Just like the economic sector, the occupational field has developed rapidly and undergone major changes in recent years, also in the context of increased digitalisation.
The increasing internationalisation of value chains has led to a change in the job profiles in almost all areas of logistics. Whereas logistics specialists used to be mainly concerned with transport, handling and storage, today they control entire value-added networks. Logistics is much more than just managing the flow of goods and picking containers. Its tasks include the market-oriented, integrated planning, design, processing and control of the entire flow of materials and associated information between companies, suppliers and customers as well as within a company.
As the complexity of the tasks increases, so does their attractiveness. The constantly changing requirements of the various markets demand flexible and permanently evolving concepts from logistics. For the responsible employee, process understanding and analytical skills, but also creativity for innovative solutions are required. Therefore, there is also a demand for highly qualified specialists in logistics, which is also increasing in the future.
Sources: Industriemagazin, URL: https://industriemagazin.at/a/fachkraeftemangel-bei-logistikern-wir-sind-kurz-vor-dem-versorgungskollaps [14.05.2020].
Abimagazin, URL: http://doku.iab.de/abi/2011/abi0311_22.pdf [14.05.2020].
Karriere.de, URL: https://www.karriere.de/arbeitsmarkt-logistik-karriere-in-der-container-welt/23040246.html [14.05.2020]
Zentralverband für Spedition und Logistik, URL: https://www.ots.at/presseaussendung/OTS_20191129_OTS0158/logistik-branche-als-innovationstreiber-digitalisierung-mehr-chance-als-bedrohung-bild [14.05.2020].

## Slide 10: Excursus: Women in logistics Market environment logistics
Making logistics jobs more attractive for women with the help of
benefits such as:
flexible working hours Working hours with consideration of family circumstances
Job sharing and childcare measures
Promotion of networking and exchange of women initiatives such as "Ladies in Logistics" and "Women in Mobility”
Positive communication
Ergonomic workstations etc..
Notes: Logistics is slowly making itself attractive to women: Women are still underrepresented in logistics today, but the trend shows that several thousand women are now working in the various logistics professions and the number is constantly increasing. Many logistics companies already offer flexible working hours, individual part-time work with consideration of family circumstances, even job sharing is partly lived. In addition, childcare measures are increasing. An important element in making logistics professions more attractive to women is the opportunity for networking with the help of initiatives such as "Ladies in Logistics" or "Women in Mobility". Positive communication also plays a decisive role. Bosch offers an example of this with its "Working Out Loud" initiative. This initiative sets an example of network-oriented work, which allows women to focus on both personal and professional goals.
Source: BVL, 2019, URL: https://www.bvl.de/files/1951/1988/2128/Begleitende_Publikation_zur_Session_Maennerdomaene.pdf [14.05.2020]

## Slide 11: Developments in freight transport - Inland navigation Market environment logistics
71 % of the total transport performance in European inland navigation is carried out in the Netherlands and Germany.
Rhine States: 84 % of the total freight transport performance
Danube countries: 16.4 % of freight transport performance
Total transport performance of inland navigation in the European Union 2018: 135 billion TKM
Chart: Annual transport performance in inland navigation in Europe
| Sand, Stones | Mineral oil products | Agricultural products | containers | chemical products | metals | waste | others
Annual transport performance in inland navigation in Europe | 0.26 | 0.25 | 0.15 | 0.11 | 0.11 | 0.06 | 0.03 | 0.03
Source: bsased on Zentralkommission der Rheinschifffahrt
Notes: Inland waterway transport in Europe is mainly concentrated in two countries, the Netherlands and Germany, where almost 70% of the total transport performance of European inland navigation is handled. In general, the Rhine States of the European Union (Belgium, the Netherlands, France and Germany) represent 84% of the total inland waterway transport performance, while the Danube States of the EU (Bulgaria, Croatia, Hungary, Austria, Romania and Slovakia) account for 16.4% of the transport performance on European waterways. The total transport performance of inland navigation in the European Union reached almost 135 billion TKM in 2018.
Source: Zentralkommission für die Rheinschifffahrt, Marktbeorbachtung 2019, URL: https://www.ccr-zkr.org/files/documents/om/om19_II_de.pdf [14.05.2020].
Picture: in Anlehnung an Zentralkommission der Rheinschiffahrt, Marktbeobachtung 2019, URL: URL: https://www.ccr-zkr.org/files/documents/om/om19_II_de.pdf [14.05.2020].

## Slide 12: Transport routes – inland navigation Market environment logistics
Rhine-Main-Danube corridor – an important link between Western and Eastern Europe
Total length: 3,504 km
Connects the port of Rotterdam (NL) with the port of Constanta (RO)
Rhine vs. Danube:
  Transport volume:4.8 times more goods are transported on the Rhine
  Length: Danube is 2.7 x longer
  Different infrastructural requirements
    Limited branching of the Danube waterway
    129 bridges span the Danube
    Population density and economic activity on the Rhine
Notes: The Rhine-Main-Danube corridor has a total length of 3,504 km and connects the port of Rotterdam (Netherlands) with the port of Constanta (Romania) and thus also 15 European countries directly by water. If one compares the Danube waterway with the Rhine, it is 2.7 times longer than the Rhine. Nevertheless, in 2017 4.8 times more goods were transported on the Rhine than on the Danube. The transport performance on the Rhine was thus 1.6 times higher than on the Danube in 2017. The limited branching of the Danube waterway allows only a spatially concentrated use, furthermore a longer pre- and post-carriage by road or rail is necessary. As a consequence, inland navigation in the Danube Region generally has a smaller share in the national modal split. However, Danube transport is characterised by longer distances compared to transport performance. The average transport distance on the Danube is about 600 km, while that of the Rhine is only about 200 km. A total of 129 bridges span the Danube from Kelheim to Sulina. Since the bridges allow a maximum of 2-3 layers of container traffic on the Danube, which would be less economical, there is practically no container traffic on the Danube. Container transport is mainly operated in the Rhine area. In addition, the Rhine has four main tributaries, which strengthen the role of the Rhine as the most important waterway in Europe. The economic activity and the high population density along the Rhine also support an increased use of this inland waterway as a mode of transport.
Source: Manual on Danube Navigation p 20, 21, 56
Picture: viadonau, Inland Navigation Europe im Manual on Danube Navigation p 44

## Slide 13: Quiz Market environment logistics
What percentage of freight transport in 2018 was transported by inland waterway throughout Europe?
6% c) 19%
16% d)7%
Quelle: viaodnau
Notes: Picture: viadonau on https://fotos.viadonau.org

## Slide 14: Agenda Development trends and innovation in logistics – focus on inland navigation
Market environment logistics
Development trends at a glance
4 Drivers for the development of innovations
Innovative transport concepts
Innovative business models

## Slide 15: Current development trends Development trends at a glance
Sustainability
  revised pricing
  use of alternative fuels (LNG, ...),
  promoting a shift to sustainable modes of transport (rail and inland waterways)
  Increased use of innovative technologies
Digitalisation/connection of logistics
  Increasing number of online purchases
  Connection with customers and other key players
Innovative transport concepts
  Synchromodality: bundling effects and elimination of prejudices can contribute to an increased use of rail and inland waterway transport
  Physical Internet: Strengthening the position of the inland vessel as part of the overall network
Notes: In general, the transport sector is facing the challenge that the volume of goods will increase strongly in the future - an increase of 50 % is predicted by 2030. At the same time, the road transport mode is already operating at full capacity for the most part, which reinforces the demand for a sustainable, multimodal transport solution. Increasing traffic jams, accidents, hurdles and inefficiencies have also increased the costs of transport, which in turn weakens the competitiveness of road transport in general. In addition, the transport sector remains heavily dependent on oil and is responsible for a large proportion of CO2 emissions. Various trends have emerged to counteract these developments. In particular, the trend towards sustainability is an increasingly relevant aspect for the transport sector in order to reduce its negative impact on the environment in the future. In addition, trends such as innovation and cooperation are an important topic in the transport sector in order to cope with the resource bottleneck with regard to transport infrastructure. In the following, the most important trends from the transport sector are described in more detail and their significance for inland navigation is discussed. In order to select the trends, these were discussed together in the course of an internal expert workshop and their significance for inland navigation assessed.
Sustainability:
Freight transport can be identified as an environmentally damaging area of logistics. In Europe, greenhouse gas emissions and traffic congestion have been identified as the most serious environmental and sustainability problems in freight transport and logistics. Due to the increasing transport volume in Europe as well as on an international level, this problem will become even more relevant in the future and the increasing need for action becomes apparent. Accordingly, the issue of sustainability is becoming increasingly important for freight transport. The catalogue of measures to counteract these developments is relatively large: changed pricing, use of alternative fuels, promotion of a shift to sustainable modes of transport such as rail and inland waterways or the increased use of innovative technologies. From the political side, it is above all the modal shift measure that is being promoted. As stated in the White Paper 2011, the European Union has set itself the goal of shifting 30% of road freight traffic exceeding a transport distance of 300 km to alternative modes of transport such as rail or inland waterways by 2030. By 2050, this figure should be more than 50%, in order to achieve a long-term reduction of CO2 emissions in the freight transport sector.
Alternative drive technologies or fuels have also been increasingly promoted in recent years. In the road transport sector, a hybrid solution of the following drive systems is conceivable: electric, liquefied natural gas (LNG) and diesel. The greatest potential for electric drive systems is seen in light vehicles. The fuel LNG (Liquefied Natural Gas) is an environmentally friendly energy source and offers the possibility to reduce emissions. This fuel is particularly interesting for inland navigation. The use of LNG could reduce climate-relevant emissions and also generate cost advantages, as the fuel is cheaper than diesel. This would also mean that conversion costs would be amortised relatively quickly. Nevertheless, there are currently no LNG-operated inland navigation vessels in Europe. Only a few pilot operations have already been realised with LNG. In addition, as already mentioned, high investments would be necessary to convert the ships themselves and also the port infrastructure so that the fuel can be stored.
This development is particularly advantageous for inland navigation vessels, as they are considered a sustainable means of transport and are also regarded as such by the European Commission. Moreover, the waterway mode of transport offers sufficient free capacity to accommodate a modal shift. Accordingly, the trend towards sustainability can be classified as particularly relevant for inland navigation.
Digitalisation/connection of logistics:
Digitalisation and networking and the associated trends Industry 4.0 and the Internet of Things are also currently relevant topics in logistics. Due to the digitalisation of society in general and the increasing number of online purchases, the logistics industry is increasingly faced with new challenges. Accordingly, networking of logistics service providers with customers and other relevant players is crucial in order to cope with the increasing transport volume. Even though the technical prerequisites may often already exist or could be implemented relatively quickly, it is still necessary to establish a corresponding basis of trust between the players. Trust is important in order to realize data exchange and to make sure that actors are willing to share all relevant data with the partners and that these data are not misused for their own purposes. Since the willingness to exchange data is often not yet given due to a lack of trust, the attitude of the actors must also be positively influenced in the future. In addition, the use of (partly) autonomous vehicles (e.g. in platooning) can, for example, make better or more efficient use of the transport infrastructure. In this way traffic jams or accidents can be avoided and transport processes optimised. Nevertheless, further tests still need to be carried out and the legal basis revised in order to realise autonomous driving in the long term.
The trend of autonomous vehicles is not as relevant for inland navigation in the near future as it is for road transport, for example, since the hazard potential of inland navigation is still predominant. Nevertheless, an open data management offers the actors of inland navigation such as shipping companies or forwarding agents the possibility to gain a quick overview of the transport flows. This way, enormous efficiency advantages can be realised even in individual processes such as smuggling through automated registration and payment. Furthermore, a rapid exchange of information allows transport processes such as transhipment and pre- and post-carriage to be optimally planned to avoid cost-intensive waiting times. Especially in ports with container handling, digitalisation is already a very present topic, as the handling of the many containers and their transhipment would hardly be possible without the use of electronic data processing. The trend towards digitalisation is already being lived out in the port of Hamburg, for example, although there is still potential for expansion. However, in order to be able to take advantage of this trend in the future in the area of inland navigation, high investments must be made in equipment and in training and further education, the security of a digital network must be ensured and international standards must be introduced.
Innovative transport concepts:
Due to the various trends, new transport concepts are constantly being created to meet the changing requirements and to integrate new developments and trends. Multimodal transport in particular has gained in importance. While intermodality is a special form of multimodal transport in which the cargo is transported in the same loading unit (e.g. container), the concept of co-modality uses the most optimal mode of transport or the most optimal combination of modes of transport. The concept of co-modality was defined by the European Commission in 2006, although the concept is hardly known in practice. An important element of co-modality is efficiency, as the aim is to plan and carry out transport operations as efficiently as possible. A further development is the concept of synchromodality, which is a combination of intermodality and co-modality. The idea of this concept, which originated in the Netherlands, is that the customer only defines basic requirements for the transport (e.g. costs and duration of the transport) and that the transport is made efficient and sustainable by a cooperative network of different actors and modes of transport. The cooperative network enables a real time change between the transport modes, which allows to react as quickly as possible to disturbances or other influences. A further development with regard to transport concepts is the Physical Internet, founded by the Canadian Benoit Montreuil. Here, goods are transported like data (e.g. sending an email). The goods or packages are sent independently and with the help of a hub network, the consignment independently searches for the most optimal route to arrive at its destination. The most important prerequisite for the Physical Internet is an open and transparent network.
Source: INE, EBU und ESO, 2011, S. 4
Psaraftis, 2016, S. 14
Institute for Transport Studies, Univerisät Leeds (UK), 2010, S. 7
Europäische Kommission, 2011, S. 10
Die Welt, URL: https://www.welt.de/motor/news/article155884171/Nutzfahrzeug-Studie.html [05.05.2020]
Pucher et al., 2011, S. 1ff
Borlenghi, et al., 2015, S. 21ff
URL: http://n.diemacher.at/1083/logistik-4 [05.05.2020]
Kauder, Hasselfeldt, & Oppermann, 2016, S. 1f
Kauder, Hasselfeldt, & Oppermann, 2016, S. 7f
Zentralverband der deutschen Seehafenbetriebe e.V., 2016, S. 1f

## Slide 16: Current development trends Development trends at a glance
Individualisation and increasing complexity of logistics
Shaped by e-commerce
Demand for smaller, individualised goods is increasing
New requirements regarding:
  Speed
  Adherence to delivery dates
  Flexibility
  Quality
Cooperation
Increasing division of labour in the economy
Increased focus on core competencies
Notes: Individualisation and increasing complexity of logistics
In order to survive in the current competitive environment, many companies have to customize the products and services they offer. In addition, customers are demanding ever shorter delivery times. Ultimately, this leads to an increasing complexity of logistics chains and poses a major challenge for logistics and its players. This development is also due to the great importance of e-commerce - especially in the B2C sector. In Austria, the retail trade in particular is characterised by online trading. Studies show that there is an increased demand for higher-value goods, whereby the weight of transport orders is decreasing. This means that customers demand smaller, individualised goods of higher value. For providers and players in logistics, this development in turn means new requirements in terms of speed, punctuality, flexibility and quality of the service offered in order to guarantee value. This consumer ordering behaviour also influences the logistics processes, which must react flexibly to the changed requirements. This development is also reflected in the increasing importance of CEP transport.
Inland navigation is also affected by the trend towards individualisation and the growing complexity of transport processes, as increasingly individual transport services reduce the possibilities of transport bundling. This in turn is a trend which is disadvantageous for inland navigation, since in this sector road transport offers the great advantage of network density and flexibility. Nevertheless, especially in conurbations, such as large cities, there may be opportunities for using inland waterways for the transport of smaller consignments. The French company "Vert Chez Vous" can be mentioned as an example.
Cooperation
Increasing globalization and thus the growing division of labor in the economy has led many companies to focus on their core competencies. As a result, more and more make-or-buy decisions have to be made and thus it is necessary to work together with other companies on a global scale. This has led to the formation of complex company and supplier networks, which in turn result in increased international flows of goods and commodities, which ultimately lead to increased freight traffic. Therefore, different challenges have arisen for freight transport, such as the increasing ecological demands on freight transport as well as the growing importance of cooperation between the different modes of transport in order to efficiently meet the increased demand for freight transport. A distinction can be made between cooperation between actors at the same level of the logistics chain (horizontal cooperation) and cooperation between actors at subsequent levels of the logistics chain (vertical cooperation).
From the perspective of logistics service providers, different reasons for horizontal or vertical cooperation can be identified. The increasing globalization and thus the increasing cost pressure (keyword low-wage countries), the high fixed costs in the transport sector and also the deregulation of the transport industry speak in favor of horizontal cooperation. Horizontal cooperation can open up new geographical markets, as international transport services can be offered. In addition, economies of scale can be exploited, allowing the existing infrastructure and means of transport to be utilised more efficiently. Finally, cost savings can also be realized. In addition, horizontal cooperations can be used to offer different logistics services, thus addressing different customers and markets. The increasing concentration of companies on their core competencies as well as the increase in competition and thus the growing time pressure in the transport industry speak in favour of vertical cooperation. Through vertical cooperation, specific services can be offered to achieve a competitive advantage. Rationalization gains can also be realized through close integration into the value chain of upstream or downstream players. An advantage for the customer is, for example, the improvement in the reliability of transport demand forecasts through longer-term cooperation.
For inland navigation, horizontal or vertical cooperation could also increase the competitiveness of the mode of transport. For example, economies of scale could lead to the efficient use of inland waterway vessels and thus also to cost advantages. Since transport by inland waterway is often international rather than national, international cooperation is also entirely possible. Cooperation could also make it easier to open up new markets. Cooperation on a vertical level could also be simplified by increasing the number of companies settling near the port. This could promote a greater integration of inland navigation into the transport chain.
Source: Wittenbrink , 2014, S. 23f
WKO, URL: https://www.wko.at/branchen/handel/Studie__Internet-Einzelhandel_2014.html [05.05.2020]
Holderied, 2005, S. 20
Manner-Romberg, Symanczyk, & Miller, 2016, S. 4
Holderied, 2005, S. 20
Pfohl, 2004, S. 141
Vahrenkamp & Kotzab, 2012, S. 18
Claus, 2015, S. 23ff

## Slide 17: Megatrends in logistics Development trends at a glance
Development trends
Logistics
Security
Climate change
Urbanisation
E-commerce
digitalisation
Mobile World
Notes: The following megatrends lead or support the development of new trends in freight transport.
Safety is an increasingly decisive factor in the transport sector. Security checks at different points in the transport chain are becoming increasingly important. In addition, the various players must ensure that the transport chain is not used for terrorist purposes.
The consequences of climate change are becoming increasingly visible, making sustainable strategies necessary.
Some measures have already been taken: emission limits for means of transport such as trucks or increased use of alternative fuels such as liquefied natural gas (LNG).
The increasing size of cities is leading to bottlenecks in the infrastructure in conurbations and poses a major challenge for logistics service providers. By bundling flows of goods outside the cities (in consolidation centers), the flow of goods into/out of the cities can be optimally designed.
E-commerce and thus online trade have a significant influence on transport volumes, as the dispatch of goods is a crucial service for customers.
Increasing digitalisation, for example, can minimize transport distances. Access to 3D printers means that spare parts can be produced where the customer needs them, making long transport routes from the manufacturer obsolete.
Most means of transport are already equipped with technical interfaces, which enables communication between them. This creates a mobile world in which transports can be coordinated via smart phones, for example. For example, you can be notified on your mobile phone when a package is delivered and can open the door for the parcel service.
Source: Lehmacher W., „Wirtschaft, Gesellschaft und Logistik 2050 in Logistik – eine Industrie, die (sich) bewegt. Strategien und Lösungen entlang der Supply Chain 4.0“ (2015), S.9-15

## Slide 18: Current development trends in freight transport Development trends at a glance
Logistics
Security
Cimate Change
Urbanization
E-commerce
Digitalisation
Mobile World
sustainability
digitalisation
individualization and increasing complexity
cooperation
innovative
transport concepts
Relevant trends for the transport sector
Notes: Among the current and relevant trends for the transport industry are
sustainability,
digitalisation/networking,
Individualisation and increasing complexity
and cooperation (these points will be discussed in more detail later in the set of slides).
The megatrends which were explained in more detail in the previous slide can be assigned to the current development trends (see graph).
Innovative transport concepts are essential for implementing these current development trends in freight transport.
Source: Lehmacher W., „Wirtschaft, Gesellschaft und Logistik 2050 in Logistik – eine Industrie, die (sich) bewegt. Strategien und Lösungen entlang der Supply Chain 4.0“ (2015), S.9-15

## Slide 19: New technologies Development trends at a glance
New technologies like
the internet of things,
Industry 4.0,
cloud computing and
3-D printing
open up new ways of cooperation and communication in the value chain.
Source: pixabay
Notes: The vision of the "Internet of Things" offers a future-oriented approach for the logistics industry. In a concrete context, it describes the autonomous transport of goods and merchandise through internal and external networks. Analogous to the flow of digital information on the Internet, logistical objects find their own paths in the "Internet of Things", whereby they flexibly decide on the most favourable route of onward transport at nodes, depending on the conditions prevailing there, and request the necessary resources.
Logistics 4.0 or the use of Physical Internet and Big Data to further optimise the flow of goods and increase the efficiency of the use of resources and the design of processes.
Whereas transport and supply chains in the past were mostly closed processes and systems of fixed defined participants, Logistics 4.0 gives the option of developing open networks from these, which can be used to achieve the best possible use of capacities and optimised process control through modularisation and interface management to and between loads and load carriers.
3D printing is also bringing about major changes for the "traditional" supply chain. The product in demand could be printed directly at the customer's site. In principle, the use of the process gradually shifts the production location towards the place of use. This results above all in a reduction of long transport flows (near sourcing), intermediate storage and buffering. For logistics service providers, the use of 3D printing means on the one hand the elimination of transport revenues. On the other hand, however, there are new business areas in which logistics service providers can establish themselves, such as supporting customers in integrating 3D printing into existing value-added networks or specialising in digital warehousing.
Source: WKO, URL: https://www.wko.at/branchen/ooe/transport-verkehr/spedition-logistik/1---4.0-Branchenleitfaden-WKOOe-Fachgruppe.pdf [14.05.2020]
Picture: www.pixabay.com

## Slide 20: New business models Development trends at a glance
New innovative business models put established companies in the logistics sector under increasing pressure.
The main reasons for the development of new, innovative business models are
Changes in the transport and logistics industry
Current development trends
New technologies
Source: pixabay
Notes: New innovative business models are putting increasing pressure on a whole range of established companies in a wide variety of industries. This also applies to the logistics industry, where all types of transport relationships (B2B, B2C and C2C) are affected by change.
The main causes identified for the development of new, innovative business models Changes in the transport and logistics industry, current development trends and new technologies. These points will be discussed in more detail in the following slides.
Source: Bearingpoint, URL: https://www.bearingpoint.com/de-de/ueber-uns/pressemitteilungen-und-medienberichte/pressemitteilungen/digitale-plattformkonzepte-pr/ [14.05.2020].
Pictures: www.pixabay.com

## Slide 21: Quiz Development trends at a glance
Which is currently no development trend in logistics?
a) Unification b) Sustainability
c) Digitalisation d) Cooperation
Notes: Picture: www.pixabay.com

## Slide 22: Agenda Development trends and innovation in logistics – focus on inland navigation
Market environment logistics
Development trends at a glance
4 Drivers for the development for innovations
Innovative transport concepts
Innovative business models

## Slide 23: Driver 1: Sustainability in freight transport
One quarter of Europe's greenhouse gas emissions come from the transport sector
Currently, around 75% of all goods in Europe are transported by truck
A modal shift to environmentally friendly modes of transport is very important in order to reduce traffic-related emissions and thus do something good for our environment!
Important evaluation criteria of modes of transport with regard to sustainability
  specific energy consumption
  Capacities for bulk and bulk goods
  external cost
  Infrastructure costs
Notes: The transport sector accounts for 25% of EU greenhouse gas emissions and this figure is rising. Transport emissions must be reduced by 90% by 2050 to achieve climate neutrality, . All modes of transport will have to contribute to this reduction. Multimodal transport must be promoted to ensure an efficient transport system. To this end, a large proportion of the 75% share of internal freight traffic currently carried by road is to be shifted to rail and inland waterways. At present, approximately 19% of all goods are transported by rail and only 6% of all goods are transported by inland waterway.
When comparing modes of transport from a sustainability perspective, various evaluation criteria can be identified. In the environmental context, specific energy consumption, freight capacities, external costs and infrastructure costs can be mentioned as important evaluation indicators.
Source: Manual on Danube Navigation p 18-21.
Europäische Kommission: Der europäische Grüne Deal, 2019, p 12f.

## Slide 24: Inland navigation as a sustainable means of transport Sustainability in freight transport
An inland vessel can transport a tonne of cargo almost four times as far as a truck with the same energy consumption
Inland vessels cause the lowest costs in terms of accidents, noise, pollution and climate
External costs
Specific energy consumption
Notes: In terms of specific energy consumption, inland navigation can be considered the most effective and therefore the most environmentally friendly mode of transport. The inland vessel can transport a tonne of cargo almost four times as far as a truck for the same energy consumption.
The external costs, i.e. those costs resulting from climate gases, air pollutants, accidents and noise, are also lowest with inland navigation. CO2 emissions in particular are comparatively low, which means that inland waterway transport can contribute to achieving the European Union's climate objectives.
Source: Manual on Danube Navigation p 19
Picture: viadonau in Manual on Danube Navigation p 18
PLANCO Consulting & Bundesanstalt für Gewässerkunde 2007 im Manual on Danube Navigation p 19

## Slide 25: Inland navigation as a sustainable means of transport Sustainability in freight transport
  Largest transport capacity: One pushed convoy with 4 pushed barges = 175 train wagons = 280 trucks = 20 km truck convoy
Mass efficiency
Infrastructure costs
  Improving the infrastructure of the Danube as a whole would cost around EUR 1.2 billion this corresponds to the construction costs of ONLY about 50 road kilometres
Notes: Compared with other modes of transport, inland waterway transport offers a significantly larger transport capacity per transport unit and can, or could, thus make an important contribution to relieving the burden on road and rail. To illustrate the mass capacity of inland navigation: An inland vessel with 4 lighters (7,000 net tonnes) can transport as much as 175 rail wagons or 280 trucks. This corresponds to a convoy of lorries of about 20 km on the motorway! An increase in freight transport on the Danube therefore means a significant reduction in traffic jams, noise pollution, pollution and accidents on the roads and a relief for the railways.
Infrastructure costs are made up of the costs for the construction and maintenance of transport routes. As natural infrastructure is usually available in the case of inland waterways, infrastructure costs and land consumption are correspondingly low. Detailed comparisons in this respect with land transport modes are available from Germany: According to these, the infrastructure costs per tonne-kilometre are around four times higher for rail or road than for waterways. According to current cost estimates for infrastructure projects in the riparian countries, the improvement of the entire infrastructure of the Danube waterway, which is almost 2,415 km long, would amount to a total of EUR 1.2 billion. This corresponds roughly to the costs incurred for the construction of about 50 km of road or rail infrastructure.
Source: Manual on Danube Navigation p 18-20
Picture: PLANCO Consulting & Bundesanstalt für Gewässerkunde 2007 im Manual on Danube Navigation , S. 19
viadonau im Manual on Danube Navigation , S. 19.

## Slide 26: Factors limiting a modal shift in favour of inland navigation Sustainability in freight transport
Accessibility
  Train and inland waterway vessel require terminals Pre- and post-carriage necessary
Transport distance
  Transhipment additional costs for train and barge
  Corresponding transport distance necessary to be competitive in comparison to truck transport
Product requirements
  Value of the goods and necessary packaging
Use of new technologies
  In most cases not yet commercially viable in inland navigation
Speed
  delivery time > 1 day
Notes: As mentioned above, modal shift in favour of sustainable transport modes such as rail and inland waterways can be limited by several factors; accessibility can be identified as the first and most important factor: given the topography of Europe, some countries have access to a wide inland waterway system, while others do not. For this reason, countries like the Netherlands, Romania and Bulgaria have a higher share of inland waterways in the modal split than countries like Latvia or Lithuania. Another aspect of accessibility is that transport by rail or inland waterways requires terminals, which makes transhipment possible. Another limiting factor is the transport distance: as transhipments lead to additional transhipment costs for rail and inland waterways, a long transport distance is required to make rail or inland waterways transport profitable. Therefore, the same transport distances are required depending on the product and the market, so that inland waterway or rail can compete with road transport The characteristics of the products shipped can also influence the decision for the means of transport. While products of high value and low volume are preferably transported by truck, products of low value and high volume should be considered for transport by inland waterway vessels or trains. This leads us to the next limiting factor: the use of new technologies, is in most cases not yet commercially feasible in inland navigation.
The last limiting factor can be the delivery time: For short delivery times, such as the 24-hour service, other modes of transport are currently not competitive with road transport. Therefore inland navigation is mainly used for transport with longer delivery times.
Source: ACEA, URL: https://www.acea.be/uploads/publications/SAG_17.pdf S.10 [14.05.2020]
Eurostat, URL: http://ec.europa.eu/eurostat/statistics-explained/index.php/Freight_transport_statistics_-_modal_split [14.05.2020].

## Slide 27: Drivers for sustainable development – European Commission White Paper 2011 Sustainability in freight transport
Oil dependence
Increasing transport volume
Greenhouse gases
Multimodality* /modal shift
  Rising demand for sustainable modes of transport
* Transport of goods using two or more modes of transport
    Modal shift targets
    2030: 30 % of road traffic > 300 km on rail/ inland waterways
    2050: 50 % of road traffic >300 km on rail/ inland waterways
     Rail & inland waterways are recognised as sustainable transport modes!
Notes: As described in the previous slide, a shift to sustainable modes of transport is necessary.
EU policy therefore tries to promote a switch to such modes of transport by means of various measures. The European Commission's 2011 White Paper "Roadmap to a Single European Transport Area - Towards a competitive and resource-efficient transport system" presented the EU's vision for transport in the future. This White Paper contains proposals for action by the EU to make transport more sustainable in the future. As rail and inland waterways are recognised as sustainable modes of transport, a modal shift towards these modes of transport should also take place. The aim is to shift 30% of road traffic exceeding 300 km to rail or inland waterways by 2030. By 2050, the figure should be 50 %.
Source: Europäische Komission, “Weissbuch - Fahrplan zu einem einheitlichen europäischen Verkehrsraum – Hin zu einem wettbewerbsorientierten und ressourcenschonenden Verkehrssystem” (2011), S. 3ff
Online: http://eur-lex.europa.eu/legal-content/de/TXT/PDF/?uri=CELEX:52011DC0144 [14.05.2020]

## Slide 28: Excursus: Alternative fuel LNG Sustainability in freight transport
LNG = Liquefied Natural Gas
Volume is reduced to -162° by cooling LNG requires 600 times less space than natural gas
Fields of application:
  Inland navigation (liquid)
  Truck (liquid)
  Industrial processes (gaseous)
First LNG filling station in Austria - Ennshafen
2 bunker stations on the Rhine (Rotterdam, Amsterdam)
Pioneers in liquefied petroleum gas as fuel for ships Norway and Scandinavian countries (deep-sea shipping)
Notes: LNG or liquefied natural gas is natural gas that is cooled to at least -162 °C, which is 600 times less than unprocessed natural gas. This is also the main advantage in connection with transport! In addition to being used as a fuel for barges and trucks, LNG can also be used for industrial processes in gas form.
The companies RAG, Ennshafen OÖ GmbH and IVECO Austria opened Austria's first filling station for LNG (Liquefied Natural Gas) in Ennshafen in Upper Austria on 26 September 2017 as part of the LNG Future Forum. These are truck-to-ship bunker stations, which means that the truck is connected to the ship that refuels it. Norway and other Scandinavian countries can be seen as pioneers for LNG. In 2009 there were already 336 ships in the LNG tanker fleet worldwide.
Source: Youtube, URL: https://www.youtube.com/watch?v=WyZTuzUzR68 [14.05.2020].
LNG Masterplan, URL: http://www.lngmasterplan.eu/images/D_111__Status_Quo__Trend_Analysis_-_Danube_and_Italy_v2.1_FINAL_2015-3-12.pdf S.24
Aymelek, URL: https://www.researchgate.net/profile/Murat_Aymelek/publication/274379729_Challenges_and_opportunities_for_LNG_as_a_ship_fuel_source_and_an_application_to_bunkering_network_optimisation/links/55e5bf9f08aecb1a7ccd4ab6.pdf S.768 [14.05.2020].

## Slide 29: Driver 2: Digitalisation/networking of logistics
  Industry 4.0 as an extension of the Internet of Things
    social developments such as online trade are leading to a growing need for transport
    increasing automation of logistics processes
    autonomous, self-organising logistics
   significantly influence the transport volume
  Networking with customers and other key players
    to cope with the increasing volume of transport
    Creation of a basis of trust
    Readiness for data exchange
  Use of (partly) autonomous vehicles (e.g. platooning)  more efficient use of transport infrastructure
Source: pixabay
Notes: Digitalisation, networking and the associated trends Industry 4.0 and the Internet of Things are also currently relevant topics in logistics. Logistics 4.0 is an extension of the underlying idea of an Internet of Things. Due to the digitalisation of society in general and the increasing number of online purchases, the logistics industry is increasingly faced with new challenges. Accordingly, networking of logistics service providers with customers and other relevant players is crucial in order to cope with the increasing volume of transport. Even though the technical prerequisites may often already exist or can be implemented relatively quickly, it is still necessary to establish a corresponding basis of trust between the players. Trust is important in order to realize data exchange and to make sure that actors are willing to share all relevant data with the partners and that these data are not misused for their own purposes. Since the willingness to exchange data is often not yet given due to a lack of trust, the attitude of the actors must also be positively influenced in the future. In addition, the use of (partly) autonomous vehicles (e.g. in platooning) can, for example, make better or more efficient use of the transport infrastructure.
Source: VDA, URL: https://www.vda.de/de/themen/innovation-und-technik/automatisiertes-fahren/platooning.html [14.05.2020]
Die Macher, URL: http://n.diemacher.at/1083/logistik-4 [14.05.2020]
Kauder, Hasselfeldt, & Oppermann, 2016, S. 1f
Bundesvereinigung Logistik (BVL) e. V., Digitalisierung in der Logistik S. 20, URL: https://www.bvl.de/positionspapier-digitalisierung [14.05.2020]
Bildquelle: www.pixabay.com

## Slide 30: Autonomous driving Digitalisation/networking of logistics
Platooning:
Several trucks are electronically connected to each other to communicate in real time
convoy formation
  Transmission of the driving behaviour
  synchronous acceleration and braking
Technologies allow a distance of a few meters
  Reduction of air resistance
enable automated systems:
  anticipatory driving
  to react to topographical conditions and
  Saving fuel
significant efficiency increase
  significant reduction of CO2 emissions
  better use of transport space
Notes: Digitalisation means that innovative solutions are now available to further optimize freight traffic on the roads. Platooning is one of the concepts that can revolutionize transport on highways. Several trucks are electronically connected to each other to communicate in real time. The vehicles are arranged in a convoy, allowing the lead vehicle to transfer its driving behaviour to the others. This enables the convoy to perform manoeuvres such as acceleration and braking synchronously for all vehicles. This technology enables trucks to drive behind each other without danger at a distance of a few metres and significantly reduces their air resistance.
In addition, automated systems enable the vehicles to react more proactively to traffic situations and topographical conditions, thus saving further fuel.
Efficient use of roadsThrough platooning, a significant increase in efficiency is achieved in the overall platoon, resulting in a significant reduction in CO2 emissions. In addition, the available traffic space is better used and the traffic flow is optimised. The more vehicles have the technology, the more effectively platooning contributes to the optimisation of freight traffic. The aim is to develop a system that is independent of manufacturers in order to ensure even more flexible application possibilities.
Source: VDA, URL: https://www.vda.de/de/themen/innovation-und-technik/automatisiertes-fahren/platooning.html [14.05.2020].

## Slide 31: Autonomous driving Digitalisation/connectivity of logistics
Ship Platooning:
Not only trucks are being researched for autonomous control options, but driverless boats are also becoming increasingly likely in shipping
Challenges like:
  competitiveness,
  Safety and
  Managing sustainability
Advanced decision support systems
  Remote-controlled manoeuvring
Notes: Many land-based transport systems are already state of the art in terms of autonomous vehicles. There are several examples of automated subways, self-propelled intralogistic vehicles or driverless transport systems (AGV) at modern container terminals.
In modern aviation, too, there are very diverse approaches to autonomous control concepts. Consequently, autonomy is also seen as an opportunity for shipping to meet the challenges of competitiveness, safety and sustainability. This includes advanced decision support systems that offer the possibility of operating ships remotely under semi- or fully automated control. For inland navigation, the trend of autonomous vehicles is not as relevant in the near future as for example for road transport, as the hazard potential of inland navigation is still predominant. Nevertheless, an open data management offers the actors of inland navigation such as shipping companies or forwarding agents the possibility to get a quick overview of the transport flows. This way, enormous efficiency advantages can be realised even in individual processes such as smuggling through automated registration and payment. Furthermore, a rapid exchange of information allows transport processes such as transhipment and pre- and post-carriage to be optimally planned to avoid cost-intensive waiting times. Especially in ports with container handling, digitalisation is already a very present topic, as the handling of the many containers and their transhipment would hardly be possible without the use of electronic data processing. The trend towards digitalisation is already being lived out in the port of Hamburg, for example, although there is still potential for expansion. However, in order to be able to take advantage of this trend in the future in the area of inland navigation, high investments must be made in equipment and in training and further education, the security of a digital network must be ensured and international standards must be introduced.
Source: Projekt Munin, http://www.unmanned-ship.org/munin/about/the-autonomus-ship/ [14.05.2020]
Youtube, URL: https://www.youtube.com/watch?v=Z5cTxSjjEXI [14.05.2020].
Projekt NOVIMAR, URL: https://www.researchgate.net/publication/330359084_Platooning_auf_Wasserstrassen_-_Erste_Ergebnisse_aus_dem_Projekt_NOVIMAR [14.05.2020]

## Slide 32: Excursus: Pioneer: "smartPORT " - Hamburg
Objective: Optimisation of land transport due to limited capacities on roads (avoidance of congestion and waiting times), connecting of traffic flows knowing when a container has to be moved
Cloud-based IT platform (SAP) used by transport and logistics partners
Control instrument - navigation inside and outside the port area taking into account all current traffic movements
Apps for truck drivers* - help to avoid traffic jams, stress and waiting times, even freight documents can be transferred via the app
Monitoring of the trucks by means of GPS
Intelligent turnouts provide information about their status in real time
Notes: The port of Hamburg is a pioneer in the field of digitalisation in connection with inland navigation. The aim of the pioneer "smartPORT Logistics" is to optimise land transport due to limited road capacity. smartPORT logistics combines economic and ecological aspects in three sub-areas: Traffic flows, infrastructure and flow of goods. An intermodal PortTraffic Center for shipping, rail and road traffic forms the basis for linking the traffic flows. Intelligent networking is a prerequisite for smooth and efficient traffic in the port of Hamburg and, ultimately, for the flow of goods. Optimum data acquisition and rapid exchange of information enable logistics companies, forwarders and agents to select the most efficient mode of transport for their operations. A cloud-based IT platform provided by SAP is used to connect all transport and logistics partners so that all relevant information (e.g. information on specific route sections) is transmitted. By monitoring truck movements using GPS, alternative routes can be recommended in real time and waiting times caused by traffic jams, for example, can be avoided. In addition, a control instrument shows the route in and out of the port and at the same time takes into account current traffic movements. Furthermore, the smartPORT has a virtual container depot that helps to avoid journeys with empty containers. A shore-side power supply from renewable energies for cruise ships will considerably reduce the environmental impact in Hamburg. Intelligent points of the port railway are equipped with sensors that transmit data in real time to a central IT system and thus provide information on their condition, enabling timely maintenance and thus reducing or eliminating downtimes.
Sources: Hafen Hamburg, URL: https://www.hamburg-port-authority.de/de/hpa-360/smartport/ [14.05.2020]

## Slide 33: Excursus: River Information Services (RIS)
Support for freight transport, passenger shipping and traffic and transport-related tasks
Improving the:
  security,
  profitability,
  reliability and
  planability of the transports
Use of advances in logistics on waterways
in Austria DoRIS: www.doris.bmvit.gv.at
Quelle: viadonau
Notes: High-quality cost- and time-saving transport services and the provision of electronic information have become a key success factor. To enable inland navigation to meet these needs, an information and management service, River Information Services (RIS), has been generated in Europe. RIS are able to support both freight transport and passenger navigation on waterways. RIS improves traffic safety, economic efficiency, reliability and transport planning. The basic idea is that RIS data are used to provide information bases to support traffic and transport-related tasks. RIS are of great value for the entire European inland navigation. Through RIS the latest advances in logistics on waterways can be used. Furthermore, reliably planned offers can be developed. RIS are a decisive factor in the development of the European inland navigation space.
Source: Manual on Danube Navigation, S.204ff.
Picture: viadonau im Manual on Danube Navigation, S. 138.

## Slide 34: Driver 3: Individualisation and increasing complexity of logistics
Customer demand for shorter delivery times ultimately leads to an increasing complexity of logistics chains
Caused by the increasing importance of online trade, especially in the B2C sector
Increasing number of online shops
Increasing demand for individualised goods new requirements for speed, adherence to delivery dates, flexibility and quality
Increasing complexity of transport processes Increasingly individual transport services reduce the possibilities of transport bundling
Notes: In order to survive in the current competitive environment, many companies have to customize the products and services they offer. In addition, customers are demanding ever shorter delivery times. Ultimately, this leads to an increasing complexity of logistics chains and poses a major challenge for logistics and its players. This development is also due to the great importance of e-commerce - especially in the B2C sector. In Austria, the retail trade in particular is characterised by online trading. Gross annual sales in Internet retailing amounted to approximately EUR 3.8 billion in 2018, which represents 5.02% of the total retail volume. Studies show that there is an increased demand for higher-value goods, whereby the weight of transport orders is declining. This means that there is a demand from customers for smaller, individualised goods of higher value. For the providers and players in logistics, this development in turn means new requirements in terms of speed, punctuality, flexibility and quality of the service offered in order to guarantee value. This consumer ordering behaviour also influences the logistics processes, which must react flexibly to the changed requirements. This development is also reflected in the increasing importance of CEP transport.
Source:
Wittenbrink , 2014, S. 23f
Holderied, 2005, S. 20
Statista, URL: https://de.statista.com/statistik/daten/studie/947968/umfrage/umsatz-im-stationaeren-handel-und-im-online-handel-in-oesterreich/ [19.05.2020]

## Slide 35: Driver 4: Cooperation in the logistics sector
The increasing globalisation and thus the increasing division of labour in the economy is providing for:
focus on core competencies increased make-or-buy decisions, global cooperation
Increase in complex company and supplier networks
Increased international flows of goods and commodities
Increased freight traffic
Distinction between horizontal and vertical cooperation
Horizontal cooperation:
Identical industry and same value-added level
Vertical cooperation:
Identical industry, at different value added levels
Notes: Increasing globalization and thus the growing division of labor in the economy has led many companies to focus on their core competencies. As a consequence, more and more make-or-buy decisions have to be made and thus it is necessary to cooperate with other companies on a global scale. Complex company and supplier networks have formed which in turn lead to increased international flows of goods and commodities, which in the end lead to an increase in freight traffic. Therefore, different challenges have arisen for freight transport, such as the increasing ecological demands on freight transport as well as the growing importance of cooperation between the various modes of transport in order to efficiently meet the increased demand for freight transport. A distinction can be made between cooperation between actors at the same level of the logistics chain (horizontal cooperation) and cooperation between actors at subsequent levels of the logistics chain (vertical cooperation).
From the perspective of logistics service providers, different reasons for horizontal or vertical cooperation can be identified.
Source:
Pfohl, 2004, S. 141
Vahrenkamp & Kotzab, 2012, S. 18, URL: http://www.springer.com/cda/content/document/cda_downloaddocument/9783642193323-c1.pdf?SGWID=0-0-45-1199838-p174123868 [14.05.2020].

## Slide 36: Horizontal vs. vertical cooperation in logistics
Horizontal:
Development of new geographical markets Offer of international transport services
Use of economies of scale; efficient utilisation of means of transport; realisation of cost savings
Offer of various logistics services
Vertical:
Offering specific services Competitive advantages
Enabling rationalisation gains
Realisation through increased settlement of companies near the port
Notes: The increasing globalisation and thus the rising cost pressure (keyword low-wage countries), the high fixed costs in the transport sector and also the deregulation of the transport industry speak in favour of horizontal cooperation. Horizontal cooperation can open up new geographical markets, as international transport services can be offered. In addition, economies of scale can be exploited, allowing the existing infrastructure and means of transport to be efficiently utilised. Finally, cost savings can also be realized. In addition, horizontal cooperations can be used to offer different logistics services, thus addressing different customers and markets.
The increasing concentration of companies on their core competencies as well as the increase in competition and thus the growing time pressure in the transport industry speak in favour of vertical cooperation. Through vertical cooperation, specific services can be offered to achieve a competitive advantage. Rationalization gains can also be realized through close integration into the value chain of upstream or downstream players. An advantage for the customer is, for example, the improvement in the reliability of transport demand forecasts through longer-term cooperation.
Source: Claus, 2015, S. 23ff

## Slide 37: Potentials for inland navigation cooperation in the logistics sector
Horizontal or vertical cooperation (also in an international context) can be
  increase the competitiveness of inland navigation,
  Enable economies of scale and thus generate an efficient utilisation of the inland waterway vessel,
  and to facilitate the development of new markets.
Source: pixabay
Cooperation on a vertical level can be simplified by increasing the number of companies settling near the port. This could promote greater integration of inland navigation into the transport chain.
Notes: For inland navigation, horizontal or vertical cooperation could also increase the competitiveness of the mode of transport. For example, economies of scale could lead to the efficient use of inland waterway vessels and thus also to cost advantages. Since transport by inland waterway is often international rather than national, international cooperation is also quite possible. Cooperation could also make it easier to open up new markets. Cooperation on a vertical level could also be simplified by increasing the number of companies settling near the port. This could promote a greater integration of inland navigation into the transport chain.
Source: Claus, 2015, p. 23ff
Picture: www.pixabay.com

## Slide 38: Summary
The current development trends have arisen in the following areas:
  Sustainability
  Digitalisation/Networking
  Individualisation and increasing complexity
  Cooperation
New development trends may favour an increased integration of inland navigation in multimodal transport systems.
Source: pixabay
Notes: In summary, new transport concepts that influence freight transport and other developments (e.g. generally increasing freight traffic, bottlenecks in transport infrastructure, etc.) are needed. Existing infrastructure bottlenecks and the negative effects of transport volume lead to new trends in the logistics industry.
The current development trends have arisen in the following areas:
Sustainability
digitalisation/Networking
Individualisation and increasing complexity
Cooperation
Picture: www.pixabay.com

## Slide 39: Quiz 4 Drivers for the development of innovative business ideas
What is NOT a limiting factor for a modal shift in favour of inland navigation?
a) Transportation speed b) Distance
c) Accessibility d) Administration expenses
Notes: Picture: viadonau auf https://fotos.viadonau.org

## Slide 40: Agenda Development trends and innovation in logistics – focus on inland navigation
Market environment logistics
4 Drivers for the development of innovations
Innovative transport concepts
Innovative business models
Development trends at a glance

## Slide 41: From Multimodality to Syncromodality and Physical Internet Innovative transport concepts
+
+
+/-
+/-
+
+
+
+
Notes: Europe is faced with the challenge that in many cases only two modes of transport (road and rail) are available, as in many areas inland waterways and the associated waterways are not yet adequately developed or are not available in terms of infrastructure. As a result, European transport chains often do not have sufficient capacity, as the infrastructure, especially in the road sector, has already reached its maximum capacity utilisation level. Furthermore, the sustainability aspect is becoming increasingly important. This means that the optimal use of existing transport resources for freight transport is becoming increasingly important in order to ensure efficient and cost-effective transport for the future. In order to guarantee an optimal utilization of the different means of transport and thus to counteract the upcoming challenges, different transport concepts have been developed in the last years
The use of different means of transport to exploit the strengths of each mode of transport is the idea of multimodality. Intermodality allows the use of different modes of transport by transporting products in the same transport unit, thus reducing handling costs. The idea of co-modality is to use the means of transport best suited to the different transport modes (depending, for example, on the product) Synchromodality combines the best aspects of the existing concepts - standardised transport units across all modes of transport, combining the strengths of the different modes of transport, avoiding unimodal transport - by adding real-time data to ensure the most efficient transport. The concept of synchronous modality can also be seen as a first step towards the Physical Internet, which was developed by the Canadian professor Benoit Montreuil.
Source: Reis, Vasco (2015): Should we keep on renaming a +35-year-old baby? In: Journal of Transport Geography 46, S. 173–179. DOI: 10.1016/j.jtrangeo.2015.06.019.
Picture: own picture.

## Slide 42: Synchromodality
Objective: Flexible and cooperative transport network using the various means of transport available
The customer can specify basic requirements such as transport costs and delivery time
Means of transport are defined by the transport company Bundling effects
Bundling effects ensure more efficient use of transport capacities and increasing use of rail and inland waterway transport
Prerequisite for success: close cooperation of all players along the supply chain
Integration of visionary transport modes supports synchromodal systems
Notes: Synchromodality aims to create a flexible and cooperative transport network by making optimum use of the various transport resources available. The main prerequisite for the concept of Synchronous Modality is that the means of transport is not defined by the customer. When applying this concept, the customer can only define basic requirements such as transport costs and delivery time. The free choice of means of transport enables bundling effects that contribute to an efficient use of transport capacities. Thus additional transport routes can be avoided, which leads to a reduction of CO2 and other emissions. By exploiting bundling effects and eliminating decision-makers' prejudices against alternative modes of transport (rail, inland waterways), the concept can contribute to an increased use of rail and inland waterway transport. By adding real-time monitoring, it will enable advantageous transport mode and route selection. This leads to an effective use of the infrastructure and a reduction of waiting times. To ensure the success of this concept a close cooperation of all actors along the supply chain is required. Members of the synchromodal transport network must coordinate with each other to achieve optimal utilization of the means of transport and at the same time ensure that all delivery deadlines are met. A lively exchange of data and mutual trust between all actors is therefore absolutely essential.
Source: Reis, Vasco (2015): Should we keep on renaming a +35-year-old baby? In: Journal of Transport Geography 46, S. 173–179. DOI: 10.1016/j.jtrangeo.2015.06.019.

## Slide 43: Synchromodality - Potentials for inland navigation Innovative transport concepts
Enabling bundling effects inland navigation becomes more attractive
Prejudices can be overcome
in line with the policy objectives modal shift
centralised selection via the means of transport neglect of personal preferences
free capacities of waterways
only 15% of the capacity of the Danube is used!
Notes: Synchromodality also offers some potential for inland waterway transport: the establishment of transhipment points enables bundling effects and thus higher volumes can be transported. Since inland waterway vessels are particularly attractive for bulk transport, this bundling has a positive effect on inland navigation.
Furthermore, current prejudices can be overcome and the image of inland navigation as a reliable transport option can be strengthened.
Furthermore, the modal shift is also in line with political objectives.
Since personal preferences are essential, among other factors, in the decision making process for transport modes, the centralisation of the decision-making process neglects personal preferences.
Another potential for inland navigation is that there are many unused waterways in Europe, e.g. only 15% of the capacity of the Danube is used.
Sources: Fraunhofer, http://www.scs.fraunhofer.de/content/dam/scs/de/dokumente/studien/Wirtschaftliche_Rahmenbedingungen_des_Gueterverkehrs.pdf p.14 [14.05.2020].
Youtube, https://www.youtube.com/watch?v=5ofhMxRRyec [14.05.2020].

## Slide 44: Syncromodality - practical example Innovative transport concepts
European Gateway Services
Rail and inland waterway connections
Overview of the transport network incl. travel times
Services of the terminals
Other services: transport planning
Notes: European Gateway Services:
EGS offers a network of rail and inland waterway connections between Rotterdam and other hinterland terminals in Europe. The website provides an overview of the transport network, including journey times, as well as the services of the individual terminals. For shipping companies, logistics service providers, transport companies and shippers, EGS also offers other services such as transport planning. Wherever possible, transports are carried out synchromodally. All customers have to do is specify the time at which the container should arrive at its destination. The transport is carried out by the most favourable mode of transport at the time and over the most favourable route. In addition to economic aspects, sustainability also plays an important role. The most optimal solution is selected from rail, inland waterway, truck or a combination of these modes of transport.
Source: European Gateway Services Website, URL: http://www.europeangatewayservices.com/de [18.05.2020]
Picture: European Gateway Services Website, URL: http://www.europeangatewayservices.com/de [18.05.2020]

## Slide 45: Vision to 2050: The Physical Internet Innovative transport concepts
Sending products over the Internet - on the same basis as information flows
open, connected network
Basis: network of hubs is based on
    physical, digital and operational interconnection
    basics of the digital internet
Example: based on data a container searches for its own way. Algorithms calculate the ideal route
Inland waterway vessels and trains preferred (environmentally friendly)
HUB
HUB
HUB
HUB
Customer
Internet
consignor
consignee
Physical Internet
Sending products over the Internet - on the same basis as information flows!
Notes: Another innovative transport concept is the Physical Internet. The Canadian professor Benoit Montreuil is considered a pioneer in this field. The basic idea of the Physical Internet is to send freight and information flows over the Internet. For example, when sending an e-mail, in most cases it is not known which provider is used by the recipient or via which "route" the e-mail reaches the recipient. One relies on the Internet to send the e-mail to the correct recipient. In the Physical Internet, this message consists of a physical object such as a packet. A network of hubs that send and receive the products is the basis for the Physical Internet (this network is modelled on the various servers on the Internet). The nearest hub to the customer / recipient carries out the last delivery. In the Physical Internet, all carriers and service providers are networked with each other to ensure efficient dispatch and use of the network. To ensure barrier-free and seamless transport, standardized PI containers, parcels, warehouses and transhipment points must be installed. These are connected to the Internet of Things and communicate with each other independently. Furthermore, processes must be standardised to minimise the risk of discrepancies. These standardised transport units and processes lead to a reliable and resilient smart network in which the units communicate almost independently. This smart network should be accessible to all actors in the supply chain (including at global level). This enables the transport units to choose the best transport route themselves and to interact with other transport units and stations. This makes human interaction almost superfluous (e.g. planning a transhipment process is no longer necessary). The connection between the actors, the infrastructure and the different modes of transport is essential for the Physical Internet and leads to comprehensive interconnectivity. The exchange of all relevant information and ensuring that data is up-to-date in real time are also crucial elements for the concept of the Physical Internet.
Sources:
Montreuil, Benoit (2011): Toward a Physical Internet: meeting the global logistics sustainability grand challenge. In: Logistics Research 3 (2), S. 71–87. DOI: 10.1007/s12159-011-0045-x.
Modulushca project (2014): Physical Internet. Online verfügbar unter https://www.youtube.com/watch?v=lltcWVNrjl0 [19.05.2020]
Picture: own diagram.

## Slide 46: Vision to 2050: The Physical Internet
Notes: The YouTube video "Towards Physical Internet Implementation: ALICE research and innovation roadmaps" explains Physical Internet in a clear and easily understandable way.
The video shows the different problems logistics is confronted with, the numerous different goods, the lack of coordination between the different modes of transport, the poor use of warehouses and the complex networks. Solutions to these problems are offered by the Physical Internet, goods are standardised, the modes of transport are linked, warehouses are better used and the supply chain becomes more coherent.
Source:
ETP Alice (2015): Towards Physical Internet Implementation: ALICE research and innovation roadmaps. URL: https://www.youtube.com/watch?v=4vc7XoEYUs8

## Slide 47: Quiz Innovative transport concepts
By which year should the Physical Internet be implemented?
a) 2040 b) 2050
c) 2022 d) 2070

## Slide 48: Agenda Development trends and innovation in logistics – focus on inland navigation
Market environment logistics
4 Drivers for the development of innovations
Innovative business models
Development trends at a glance
Innovative transport concepts

## Slide 49: Innovative business models in the logistics sector
In the future, new business models will develop in the following four areas in particular:
booking and optimization platforms
carriers and terminal operators
supply chain specialists
service providers
Notes: According to experts, new business models will develop in four areas in particular:
1. booking and optimization platforms
2. carriers and terminal operators
3. supply chain specialists
4. service provider
The four business models are described in the following slides.
Source: Kalaidos Fachhochschule Schweiz, URL: https://www.kalaidos-fh.ch/Blogs/Posts/2017/01/uf-1065-Logistik-vier-Geschaeftsmodelle [04.05.2020]

## Slide 50: Booking and optimization platforms Innovative business models in the logistics sector
More cost-effective and efficient design of transport processes
Direct networking of customers and logistics service providers is made possible
Direct B2C access
Optimisation of transport capacity  Reduction of freight costs
Cooperation among logistics companies makes it possible to act as a neutral platform provider.
Notes: Booking and optimization platforms can make the traditional business of transport companies more efficient and cost-effective. The direct networking of customers and logistics service providers enables optimised processing and efficient transport capacity utilisation, which in turn reduces freight costs. It is advantageous for logistics companies to enter into cooperation agreements with other logistics companies in order to be able to act jointly as a neutral platform provider. With the help of cooperations, it is possible to achieve a greater reach.
To be able to act jointly as a neutral platform provider, logistics companies should therefore examine cooperation models.
Source: Kanal Egal, URL: https://www.kanal-egal.de/wie-digitale-geschaeftsmodelle-die-logistikbranche-veraendern/ [19.05.2020]
iBusiness, URL: https://www.ibusiness.de/aktuell/db/568814veg.html [19.05.2020]
Erste Bank und Sparkasse, URL: https://newsroom.sparkasse.at/2016/11/03/logistik-4-0-vier-geschaeftsmodelle-digitalen-zukunft/34626 [18.05.2020].

## Slide 51: Booking and optimization platforms Innovative business models in the logistics sector
Practical example:
Bargelink
Offers cargo and free capacities
Notes: Bargelink:
On this European online platform, users can offer or search for loads and free capacities. Bargelink.com is interesting for all players in the European inland navigation.
Source: Bargelink Website, URL: http://direct.bargelink.com/ [04.05.2020]
Picture: Bargelink Website, URL: http://direct.bargelink.com/ [04.05.2020]

## Slide 52: Booking and optimization platforms Innovative business models in the logistics sector
Practical example:
Uship
Online marketplace to offer or inquire about transport services  Focus on trucks
Transport of various goods (heavy loads, household goods, removals, animals, are organized.
Notes: UShip:
Transport services can be offered or requested on this online marketplace. However, the focus is on trucks. The transport of palletised goods, but also heavy loads, household goods, removals, vehicles and animals can be handled.
Source: UShip Website, https://learn.uship.com/carriers/getting-started/ [18.05.2020]
Picture: UShip Website, https://learn.uship.com/carriers/getting-started/ [18.05.2020]

## Slide 53: Carriers and terminal operators Innovative business models in the logistics sector
Still an essential part of the value chain
In order to optimise capacity utilisation and costs, economies of scale and the latest technologies must be used
Special freight packages should be designed to avoid being dependent on orders from booking platforms only  small companies save booking fees
Own online platforms in cooperation with other terminal operators would be conceivable
Notes: Carriers and terminal operators are an essential part of the value chain. In the future, they will have to use economies of scale & latest technologies to optimize utilization and costs. Special freight packages should be designed to not only depend on the orders of booking platforms, thus small companies with simple logistics chains could save the booking fees of the platforms. The development of an own online platform in cooperation with other freight carriers or terminal operators would be conceivable for this purpose.
Source: Kanal Egal, URL: https://www.kanal-egal.de/wie-digitale-geschaeftsmodelle-die-logistikbranche-veraendern/ [19.05.2020]
iBusiness, URL: https://www.ibusiness.de/aktuell/db/568814veg.html [19.05.2020]
Erste Bank und Sparkasse, URL: https://newsroom.sparkasse.at/2016/11/03/logistik-4-0-vier-geschaeftsmodelle-digitalen-zukunft/34626 [18.05.2020].

## Slide 54: Carriers and terminal operators Innovative business models in the logistics sector
Practical example:
Cargo Center Graz (CCG)
Neutral booking platform for combined transport
Bundling of transport requirements of all logistics companies active in combined transport
Organisation of block train transports to various ports in Germany, Slovenia, Italy and Austria
Notes: Cargo Center Graz (CCG): The neutral logistics platform of Cargo Center Graz allows the bundling of transport requirements of all logistics companies operating in combined transport. There are several daily block train connections around the port of Koper (Slovenia) to Neuss (Germany) and other destinations. Additional services are also offered. For example, the organisation of pre-carriage and onward carriage is organised as additional services.
Source: Cargo Center Graz Website, URL: http://www.cargo-center-graz.at/dienstleistungen/logistik-plattform/ [18.05.2020]
Picture: Cargo Center Graz Website, URL: http://www.cargo-center-graz.at/dienstleistungen/logistik-plattform/ [18.05.2020]

## Slide 55: Supply chain specialists Innovative business models in the logistics sector
Handling of complex delivery processes  requires industry-specific know-how
For more efficient and transparent design  Automation of processes
Major challenge: to be innovative while remaining competitive
Cooperation with service providers makes sense
Notes: Supply chain specialists require industry-specific know-how to handle complex supply processes. In order to make complex supply chains more efficient and transparent, the automation of processes must also make greater progress. One of the biggest challenges for supply chain specialists is to be innovative and not to miss technological leaps at the same time, and to remain competitive in terms of price. Cooperation with service providers would make sense.
Source: iBusiness, URL: https://www.ibusiness.de/aktuell/db/568814veg.html [19.05.2020]

## Slide 56: Service providers Innovative business models in the logistics sector
Service providers provide software products and solutions for the collection and systematic analysis of large amounts of data
They are therefore the core of digital logistics
Offered are e.g. online payment systems, GPS tracking or automated customs clearance
Valid data (in real time) and seamless connection are a prerequisite
Notes: Service providers provide software products and solutions for the collection and systematic analysis of large amounts of data and other digital services. The range of services extends from online payment systems to automated customs clearance. Service providers are thus the core of digital logistics. It is through service providers that the processing of transactions becomes possible in the first place. Access to valid data, in real time and seamless connection with partners is a prerequisite for the success of digital solutions and software products.
Source: Kanal Egal, URL: https://www.kanal-egal.de/wie-digitale-geschaeftsmodelle-die-logistikbranche-veraendern/ [19.05.2020]
iBusiness, URL: https://www.ibusiness.de/aktuell/db/568814veg.html [19.05.2020]

## Slide 57: Relevant business models for inland navigation
Innovative and data-driven business models are also interesting for inland navigation
Major challenge: availability and selection of suitable data (the data volume is constantly increasing, but only a few can be used directly)
Technical and structural adjustments are essential for the implementation of innovative, data-driven business models
Notes: Inland navigation is also influenced by these business models. Especially the trend towards digitalisation and the resulting business models are very relevant for inland navigation. A major challenge for the implementation of innovative and data-driven business models is to find suitable data. Although the volume of data is constantly increasing, the data can only be used directly to a limited extent, many of them are even still recorded in analogue form.
Source: Deutsches Zentrum für innovative Binnenschifffahrt, Studie- Digitalisierung in der Binnenschifffahrt, URL: https://d-zib.eu/wp-content/uploads/sites/2/2019/02/190212-Handout-EIBIP.pdf [18.05.2020]

## Slide 58: Cooperation and digitalisation Relevant business models for inland navigation
Practical examples
Paris (France):
Franprix
Deliveries to supermarkets by inland waterway
Bundling of goods in distribution centres
Return transport of the empty boxes to the distribution centre
.
Source: pixabay
Notes: Paris (France): As the road network in Paris is chronically congested, transport service providers are increasingly using the Seine as a transport route again. Various solutions have been found here, especially for the growing e-commerce. The supermarkets of Franprix are supplied in Paris by inland waterway. The goods are bundled in advance in distribution centers, then transported to Paris by barge and from there the last mile is covered by truck. The empty boxes are then transported back to the distribution center. This alternative is worthwhile compared to unimodal transport by truck, even though the transport unit is handled twice.
Source: The Guardian, URL: https://www.theguardian.com/cities/2016/mar/01/paris-french-retailer-franpix-delivers-goods-by-boat-river-seine-transport-water-future-urban-logistics [18.05.2020]
Bildquelle: www.pixabay.com

## Slide 59: Cooperation and digitalisation Relevant business models for inland navigation
Practical examples
Amsterdam (Netherlands)
DHL express
makes use of the well-developed and underutilised canal and waterway network
Floating distribution centre in the city centre
Mariteam Mokum
Logistics services in the canals of Amsterdam Transport of waste containers, bulk containers, skeleton containers or pallets
Equipped with a hybrid drive emission-free and low-noise transport
Notes: Amsterdam (Netherlands)
DHL Express: In Amsterdam, DHL also makes use of the well-developed and underutilized canal and waterway network. The DHL Express serves as a floating distribution centre in the city centre. Using a special schedule, the boat travels to various stations throughout the day, distributing letters and parcels throughout the city. By combining it with bicycle couriers, the number of DHL delivery vehicles in Amsterdam's inner city area has been reduced.
Mariteam Mokum: "Since autumn 2010, this company has been offering logistics services in the Amsterdam canals, which can transport waste containers, bulk containers, skeleton containers and pallets. The maximum loading capacity of the "City Suppliers" is 85 m³ (equivalent to 38 waste containers or 57 Euro pallets). Equipped with a hybrid drive, the ship can transport locally emission-free and quietly. The ship is mainly used to supply catering establishments or to transport the waste. Even building materials or larger pieces of freight can be easily transported into the city.
Source: Zukunft Mobilität, URL: http://www.zukunft-mobilitaet.net/117213/binnenschifffahrt-seeschifffahrt/innenstadtlogistik-binnenschiff-lastenrad-amsterdam-utrecht-paris/ [18.05.2020].]
Best Practice Factory for Freight Transport, URL: http://www.bestfact.net/mokum-mariteam/ [18.05.2020].

## Slide 60: Quiz Innovative business models
In which areas will no new business models be developed in the future?
a) Booking and optimization platforms
b) Carriers and terminal operators
c) Analogue driving time recording
d) Service Provider
Notes: In which areas will no new business models be developed in the future?
c) Analogue driving time recording

## Slide 61: Memory Final exercise 1
First divide into groups, each group then creates a memory on the topic "Development trends and innovations in logistics - focus on inland navigation".
Once all groups have created their memory, the groups swap among themselves so that each group plays through the memory of another group.
Quelle: pixabay
Notes: This exercise is suitable for groups of up to 5 people.
Duration (including playing through the memory): 45 min

## Slide 62: Mindmap Final exercise 2
Design a mind map on the most important topics of the presentation "Development trends and innovations in logistics - focus on inland navigation".
Entwicklungs-trends und Innovationen
Current development trends in freight transport
digitalisation
Innovative transport concepts
Sustainability in freight transport
Individualization and increasing complexity
Cooperation
Innovative business models
Notes: This exercise is suitable for groups of up to 5 people.
Duration: 45 min

## Slide 63: Sources A-E
Abimagazin, URL: http://doku.iab.de/abi/2011/abi0311_22.pdf [14.05.2020].
ACEA, URL: https://www.acea.be/uploads/publications/SAG_17.pdf S.10 [14.05.2020]
Aymelek, URL: https://www.researchgate.net/profile/Murat_Aymelek/publication/274379729_Challenges_and_opportunities_for_LNG_as_a_ship_fuel_source_and_an_application_to_bunkering_network_optimisation/links/55e5bf9f08aecb1a7ccd4ab6.pdf S.768 [14.05.2020].
Bargelink Website, URL: http://direct.bargelink.com/ [04.05.2020]Bearingpoint, URL: https://www.bearingpoint.com/de-de/ueber-uns/pressemitteilungen-und-medienberichte/pressemitteilungen/digitale-plattformkonzepte-pr/ [14.05.2020].
Best Practice Factory for Freight Transport, URL: http://www.bestfact.net/mokum-mariteam/ [18.05.2020].
Bundesvereinigung Logistik (BVL) e. V., Digitalisierung in der Logistik S. 20, URL: https://www.bvl.de/positionspapier-digitalisierung [14.05.2020].
BVL, 2019, URL: https://www.bvl.de/files/1951/1988/2128/Begleitende_Publikation_zur_Session_Maennerdomaene.pdf [14.05.2020].
Cargo Center Graz Website, URL: http://www.cargo-center-graz.at/dienstleistungen/logistik-plattform/ [18.05.2020]
Deutsches Zentrum für innovative Binnenschifffahrt, Studie- Digitalisierung in der Binnenschifffahrt, URL: https://d-zib.eu/wp-content/uploads/sites/2/2019/02/190212-Handout-EIBIP.pdf [18.05.2020]
Die Macher, URL: http://n.diemacher.at/1083/logistik-4 [14.05.2020] .
Der Wirtschaftsingenieur, URL: https://www.der-wirtschaftsingenieur.de/index.php/die-7-dimensionen-der-logistik/ [14.05.2020].
Die Welt, URL: URL: https://www.welt.de/motor/news/article155884171/Nutzfahrzeug-Studie.html [05.05.2020].
Erste Bank und Sparkasse, URL: https://newsroom.sparkasse.at/2016/11/03/logistik-4-0-vier-geschaeftsmodelle-digitalen-zukunft/34626 [18.05.2020].
Europäische Kommission: Der europäische Grüne Deal, 2019.
Europäische Komission, “Weissbuch - Fahrplan zu einem einheitlichen europäischen Verkehrsraum – Hin zu einem wettbewerbsorientierten und ressourcenschonenden Verkehrssystem” (2011).
European Gateway Services Website, URL: http://www.europeangatewayservices.com/de [18.05.2020]
Eurostat, “Freight transport statistics – modal split”, (2020), URL: http://ec.europa.eu/eurostat/statistics-explained/index.php/Freight_transport_statistics_-_modal_split [28.04.2020].

## Slide 64: Sources F-V
Fraunhofer, http://www.scs.fraunhofer.de/content/dam/scs/de/dokumente/studien/Wirtschaftliche_Rahmenbedingungen_des_Gueterverkehrs.pdf p.14 [14.05.2020].
Fraunhofer FIT (2016), Blockchain: Gundlagen, Anwendungen und Potenziale – White Paper, URL: https://www.fit.fraunhofer.de/content/dam/fit/de/documents/Blockchain_WhitePaper_Grundlagen-Anwendungen-Potentiale.pdf [14.05.2020].
Fraunhofer, URL: https://www.iml.fraunhofer.de/de/abteilungen/b3/verkehrslogistik/dienstleistungen/synchromodalitaet.html [18.05.2020].
Hafen Hamburg, URL: https://www.hamburg-port-authority.de/de/hpa-360/smartport/ [14.05.2020].
iBusiness, URL: https://www.ibusiness.de/aktuell/db/568814veg.html [19.05.2020].
Industriemagazin, URL: https://industriemagazin.at/a/fachkraeftemangel-bei-logistikern-wir-sind-kurz-vor-dem-versorgungskollaps [14.05.2020].
Kalaidos Fachhochschule Schweiz, URL: https://www.kalaidos-fh.ch/Blogs/Posts/2017/01/uf-1065-Logistik-vier-Geschaeftsmodelle [04.05.2020]
Kanal Egal, URL: https://www.kanal-egal.de/wie-digitale-geschaeftsmodelle-die-logistikbranche-veraendern/ [19.05.2020]
Karriere.de, URL: https://www.karriere.de/arbeitsmarkt-logistik-karriere-in-der-container-welt/23040246.html [14.05.2020].
Lehmacher W., „Wirtschaft, Gesellschaft und Logistik 2050 in Logistik – eine Industrie, die (sich) bewegt. Strategien und Lösungen entlang der Supply Chain 4.0“ (2015)
LNG Masterplan, URL: http://www.lngmasterplan.eu/images/D_111__Status_Quo__Trend_Analysis_-_Danube_and_Italy_v2.1_FINAL_2015-3-12.pdf
Montreuil, Benoit (2011): Toward a Physical Internet: meeting the global logistics sustainability grand challenge. In: Logistics Research 3 (2), S. 71–87. DOI: 10.1007/s12159-011-0045-x.
Modulushca project (2014): Physical Internet. Online verfügbar unter https://www.youtube.com/watch?v=lltcWVNrjl0 [19.05.2020]
Physical Internet Manifest, URL: https://de.slideshare.net/physical_internet/physical-internet-manifest-19-2011-0426-mled-ger [14.05.2020].
OPEN Insights, https://www.openinsights.de/so-funktioniert-das-blockchain/ [14.05.2020].
Projekt Munin, http://www.unmanned-ship.org/munin/about/the-autonomus-ship/ [14.05.2020].
Projekt NOVIMAR, URL: https://www.researchgate.net/publication/330359084_Platooning_auf_Wasserstrassen_-_Erste_Ergebnisse_aus_dem_Projekt_NOVIMAR [14.05.2020]
Reis, Vasco (2015): Should we keep on renaming a +35-year-old baby? In: Journal of Transport Geography 46, S. 173–179. DOI: 10.1016/j.jtrangeo.2015.06.019
T3, URL: https://t3n.de/magazin/innovative-logistik-trends-onlinehandel-zukunftspaket-238987/ [14.05.2020].
The Guardian, URL: https://www.theguardian.com/cities/2016/mar/01/paris-french-retailer-franpix-delivers-goods-by-boat-river-seine-transport-water-future-urban-logistics [18.05.2020].
Transportlogistic, URL: https://www.transportlogistic.de/de/messe/industry-insights/logistikkonzepte-der-zukunft/ [14.05.2020].
UShip Website, https://learn.uship.com/carriers/getting-started/ [18.05.2020]
Vahrenkamp & Kotzab, 2012, S. 18, URL: http://www.springer.com/cda/content/document/cda_downloaddocument/9783642193323-c1.pdf?SGWID=0-0-45-1199838-p174123868 [14.05.2020].
VDA, URL: https://www.vda.de/de/themen/innovation-und-technik/automatisiertes-fahren/platooning.html [14.05.2020].
viadonau (2019): Handbuch der Donauschifffahrt, Wien.

## Slide 65: Sources W-Z
WKO, URL: https://www.wko.at/branchen/handel/Studie__Internet-Einzelhandel_2014.html [05.05.2020]
WKO, URL: https://www.wko.at/service/aussenwirtschaft/logistik-branche-struktur-zukunft-trends.html [14.05.2020].
WKO, URL: https://www.wko.at/branchen/ooe/transport-verkehr/spedition-logistik/1---4.0-Branchenleitfaden-WKOOe-Fachgruppe.pdf [14.05.2020].
Youtube, URL: https://www.youtube.com/watch?v=WyZTuzUzR68 [14.05.2020].
Youtube, URL: https://www.youtube.com/watch?v=Z5cTxSjjEXI [14.05.2020].
Youtube, https://www.youtube.com/watch?v=5ofhMxRRyec [14.05.2020].
Youtube, https://www.youtube.com/watch?v=lltcWVNrjl0 [14.05.2020].
Zentralkommission für die Rheinschifffahrt, Marktbeorbachtung 2019, URL: https://www.ccr-zkr.org/files/documents/om/om19_II_de.pdf [14.05.2020].
Zentralverband für Spedition und Logistik, URL: https://www.ots.at/presseaussendung/OTS_20191129_OTS0158/logistik-branche-als-innovationstreiber-digitalisierung-mehr-chance-als-bedrohung-bild [14.05.2020].
Zukunft Mobilität, URL: http://www.zukunft-mobilitaet.net/117213/binnenschifffahrt-seeschifffahrt/innenstadtlogistik-binnenschiff-lastenrad-amsterdam-utrecht-paris/ [18.05.2020].

## Slide 66: Further Information
We hope our set of slides has met your expectations!
- you are free to use, adapt and share this slides and to use it for your lectures.
For questions and feedback please do not hesitate to contact us:
rewway@fh-steyr.at
Further set of slides are available at:
http://www.rewway.at/en/teaching-materials/bundles/
Maybe you are interested in booking a Transport School Lab,
a guest lecture or an excursion?
http://www.rewway.at/en/services/